## Slide 1: Practical 2 Use of ping, tracert/traceroute, ipconfig/ifconfig, route, and arp
Notes: help test connections, view network settings, track packet paths, manage routing tables, and check hardware address maps to solve computer network problems.

## Slide 2: Ping
Ping
Test if a remote computer or website is online and reachable.
Measure round-trip time (latency) in milliseconds for data packets.
Check for packet loss to see if the network connection is stable.
Ping Examples
Test connection: ping google.com
checks if Google's servers are reachable.
Test local card: ping 127.0.0.1
tests your own network card (localhost).
ping -n 5 192.168.1.1
Ping the target exactly 5 times and stop by itself.
Continuous ping: ping -t 192.168.1.1
pings your router continuously on Windows.
NOTE: Press Ctrl + C to stop
Limit packet count: ping -c 4 192.168.1.1
sends exactly 4 packets on Linux

## Slide 3: Tracert / Traceroute
Tracert / Traceroute
Trace the exact multi-hop path that data packets take to reach a destination.
Identify which specific router or network link is causing delays or failures.
Use tracert on Windows and traceroute on Linux/macOS.
Tracert / Traceroute Examples
Trace path: tracert amazon.com
tracks every router hop to Amazon on Windows.
Linux trace: traceroute amazon.com
performs the same path trace on Linux.
Skip name lookup: tracert -d 8.8.8.8
speeds up the trace by hiding domain names.

## Slide 4: Ipconfig / Ifconfig
Ipconfig / Ifconfig
Display current TCP/IP network configuration details for a device.
Show local IP addresses, subnet masks, and default gateways (routers).
Use ipconfig on Windows and ifconfig (or ip) on Linux/macOS.
Ipconfig / Ifconfig Examples
View all settings: ipconfig /all
shows detailed configuration, including DNS, on Windows.
Renew IP: ipconfig /release followed by ipconfig /renew gets a new IP from DHCP.
Linux configuration: ifconfig or ip addr show displays active interface details on Linux.

## Slide 5: Route
Route
View and manage the local IP routing table on a computer.
Add, delete, or modify static routes to control how network traffic is directed.
Diagnose why traffic takes a specific gateway or fails to reach a separate subnet.
Route Examples
View table: route print
shows the active Windows routing table.
Linux table: route -n or ip route
views the table on Linux.
Add path: route add 10.0.0.0 mask 255.0.0.0 192.168.1.254
adds a static route.
Delete path: route delete 10.0.0.0
removes the created static route.

## Slide 6: Arp
Arp
View and manage the Address Resolution Protocol (ARP) cache.
Display mappings of known IP addresses to physical MAC addresses on the local network.
Troubleshoot local hardware communication issues using commands like arp -a.
Arp Examples
View cache: arp -a
lists all current IP-to-MAC address mappings.
Clear entry: arp -d 192.168.1.5
deletes a specific device mapping from the cache.
Static mapping: arp -s 192.168.1.5 00-aa-00-62-c6-09
binds an IP permanently to a MAC.

## Slide 7: Key Behavioral Differences To Remember
Infinite vs. Finite Pings:
Windows pings exactly 4 times by default and stops.
Linux pings indefinitely until you press Ctrl + C.
Packet Tracer pings exactly 4 times on a Host PC, but a Cisco Router CLI pings exactly 5 times by default.
Mac Address Formats:
Pay close attention to hardware formatting. Windows uses hyphens (00-aa-...),
Linux uses colons (00:aa:...), and
Cisco network hardware always uses dots every four characters (00aa.0062....).
Packet Tracer PC Limitations: Simulated computers in Packet Tracer do not support advanced terminal commands for modifying routes or hardware mappings. You must use the simulated graphical user interface (GUI) properties windows instead.

## Slide 8
Network Utility / Action | Windows Command | Linux / macOS Command | Packet Tracer (Host PC) | Packet Tracer (Router/Switch CLI)
Ping (Standard) | ping 192.168.1.1 | ping -c 4 192.168.1.1 | ping 192.168.1.1 | ping 192.168.1.1
Ping (Continuous) | ping -t 192.168.1.1 | ping 192.168.1.1 | Not Supported | Not Supported
Trace Route Path | tracert 10.0.0.1 | traceroute 10.0.0.1 | tracert 10.0.0.1 | traceroute 10.0.0.1
View Basic IP Settings | ipconfig | ip addr | ipconfig | show ip interface brief
View Detailed IP/DNS | ipconfig /all | ifconfig or ip a | ipconfig /all | show interfaces
Renew DHCP Address | ipconfig /renew | dhclient | ipconfig /renew | renew dhcp [interface]
View IP Routing Table | route print | ip route or route -n | Not Supported (Use GUI) | show ip route
Add Manual Static Route | route add 10.0.0.0 mask 255.255.255.0 192.168.1.254 | ip route add 10.0.0.0/24 via 192.168.1.254 | Not Supported (Use GUI) | ip route 10.0.0.0 255.255.255.0 192.168.1.254
Delete Static Route | route delete 10.0.0.0 | ip route del 10.0.0.0/24 | Not Supported (Use GUI) | no ip route 10.0.0.0 255.255.255.0
View Local ARP Cache | arp -a | ip neigh or arp -an | arp -a | show arp
Add Static ARP Entry | arp -s 192.168.1.5 00-aa-00-62-c6-09 | arp -s 192.168.1.5 00:aa:00:62:c6:09 | Not Supported | arp 192.168.1.5 00aa.0062.c609 arpa
Clear ARP Cache / Entry | arp -d * or arp -d 192.168.1.5 | ip neigh flush all | arp -d | clear arp-cache